## Slide 1
Technical Note
V430-F Copy AOIs for Rockwell Studio 5000
February 23, 2022

## Slide 2: V430-F Copy AOIs Capabilities
Five AOIs provided to copy the V430-F EtherNet/IP Input & Output Assemblies
Input Small (100), Output Legacy (198)
  V430_Copy_Input_Small_100_AOI.L5X
Input Large (101), Output Legacy (198)
  V430_Copy_Input_Large_101_AOI.L5X
Input MXLSLC (102), Output (197)
  V430_Copy_Input_MXLSLC_102_AOI.L5X
Input 1 Decode (103), Output (197)
  V430_Copy_Input_1_Decode_103_AOI.L5X
Input 4 Decode (104), Output (197)
  V430_Copy_Input_4_Decode_104_AOI.L5X

## Slide 3: V430-F Copy AOI Requirements
AOI: V430_Copy_Input_xxxxxx_###_AOI.L5X
Developed for CompactLogix PLCs using Rockwell Studio 5000 v33
V430-F must be on same subnet as Rockwell CompactLogix PLC
V430-F EIP Assemblies - Must use V430-F assemblies defined on slide 2

## Slide 4: Copy V430-F EIP Input and Output Assemblies
Example: V430_Copy_Input_MXLSLC_102_AOI.L5X
AOI logic copies every scan
Input: Connection_Input → Assembly_Input
Output: Assembly_Output → Connection_Output
Assembly_Input, Assembly_Output are user defined data types for easier data access.

## Slide 5: V430-F Copy AOI Parameters
All parameters are required
Parameter | Description
AOI Instance Name | User Tag associated with this instance of the V430-F Copy AOI
Assembly_Input | V430 user defined Input Assembly tag
Assembly_Output | V430 user defined Output Assembly tag
Connection_Input | V430 EtherNet/IP Input Assembly memory
Connection_Output | V430 EtherNet/IP Output Assembly memory

## Slide 6: V430-F Copy AOI Operation
V430 Copy AOI designed to copy data every scan

## Slide 7: Install V430-F EDS file into Studio 5000
Tools (menu) → EDS Hardware Installation Tool
Click Next
Select Register and EDS
Click Next
2
3
4

## Slide 8: Install V430-F EDS file into Studio 5000
Register a single file
Browse your PC for the V430-F EDS file
Click Next
Click Next in the EDS File Installation Test Results window
5
6
7
8

## Slide 9: Install V430-F EDS file into Studio 5000
Click Next in Change Graphic Image window
Click Next in Final Task Summary window
Click Finish to complete the EDS installation
11
9
10

## Slide 10: Add V430-F EtherNet/IP to Studio 5000 project
In the Controller Organizer, Open I/O Configuration, right click on Ethernet and select New Module
12

## Slide 11: Select V430 Input Module
Type Omron Microscan in the filter box
Select the catalog number that starts with V430 and click Create
Name your V430-F and enter the IP address
Click Change button
14
16

## Slide 12: Select Desired Input Module Definition
Click on the Name drop down selection. In this example Input MXLSLC was selected.
Click the OK button
At the prompt asking “Change module definition?”, click Yes
18
20
Confirm the Module settings match what is shown and click OK

## Slide 13: Confirm V430-F Added to PLC project
Click Close on the Select Module dialog
Confirm V430 is added under Ethernet
22

## Slide 14: Import Add-On Instruction -
In the Controller Organizer, open Assets folder
Right click on Add-On Instruction and select Import Add On-Instruction
Select AOI that matches the selected V430-F Input Module (Item 17, Slide 12) and click Open.
2
4
The Import Configuration dialog provides details on the imported AOI. Click OK when ready to continue

## Slide 15: Insert V430 Copy AOI into MainRoutine
Expand the folder Tasks, MainTask, MainProgram. Double click on MainRoutine
Drag the V430 Copy AOI into rung 0
8
9

## Slide 16: Set V430 Copy Instance Name
Right click the first element and create a New Tag.
Enter the desired name for this instance and click Create
7

## Slide 17: Set Assembly_Input and Assembly_Output
Right click the Assembly_Input field and create a New Tag.
Enter the desired name and click Create. This tag will be used to retrieve data from the V430-F (e.g., Decoding, Trigger Acknowledge)
Right click the Assembly_Output field and create a New Tag.
Enter the desired name and click Create. This tag will be used to send data to the V430-F (e.g., Trigger)
12
14

## Slide 18: Set Connection_Input and Connection_Output
Double Click on the Connection_Input field. Click the drop down box and expand the V430 (or the name used when adding the V430 module to Ethernet). Select the item V430:I1.Data
Double Click on the Connection_Output field. Click the drop down box and expand the V430 (or the name used when adding the V430 module to Ethernet). Select the item V430:O1.Data
16
17

## Slide 19: Download to PLC and Run
Download the project to the PLC
Confirm PLC I/O OK
In the Controller Organizer, expand MainProgram and double click Parameters and Local Tags.
Select Monitor Tags to control / monitor PLC tags