## Slide 1
Technical Note
V430-F Monitor AOI for Rockwell Studio 5000
January 12, 2023

## Slide 2: V430-F Monitor AOI Capabilities
This AOI provides the following functionality:
Monitor V430-F via EtherNet/IP to detect read cycle
  Can be used with V430 Read Cycle: Trigger or Start / Stop
  Intended to monitor V430 when used with I/O trigger
  Can be used with Serial, or EtherNet/IP trigger
    V430_Trigger_Input_MXLSLC_102_AOI.L5X better choice if PLC is controlling trigger
  Barcode string output only on good read
  Error on failed read

## Slide 3: V430-F Monitor AOI Requirements
AOI: V430_Monitor_Input_MXLSLC_102_AOI.L5X
Developed for CompactLogix PLCs using Rockwell Studio 5000 v33
V430-F must be on same subnet as Rockwell CompactLogix PLC
V430-F EIP Assemblies - Input MXLSLC (102) and Output (197) must be used
V430-F read cycle: Triggered or Start / Stop. Presentation (Continuous) mode not supported.
V430-F End of Read Cycle Mode: Timeout

## Slide 4: Copy V430-F EIP Input and Output Assemblies
V430_Copy_Input_MXLSLC_102_AOI.L5X
AOI logic copies every scan
Input: Connection_Input → Assembly_Input
Output: Assembly_Output → Connection_Output
Assembly_Input, Assembly_Output are user defined data types for easier data access.

## Slide 5: V430-F Monitor AOI Operation - Disabled
Start_Monitor = FALSE
Not Monitoring V430
  Monitor_Active, Done, Busy, Error = FALSE
  ErrorID, Trig_Count, Read_Count = 0
  Barcode, ErrorMSG = ‘’ (cleared, length = 0)

## Slide 6: V430-F Monitor AOI Operation – Good Read
Start_Monitor = TRUE
V430-F Monitor AOI logic
  Confirm V430 in Run Mode
  Wait until V430 trigger counter increments
  Busy = TRUE, Done, Error = FALSE
  Wait for Pass / Fail
    Read Cycle Pass
      Busy = FALSE, Done = TRUE , Error = FALSE
      ErrorID = 0, ErrorMSG = ‘’ (cleared, length = 0)
      Barode = decoded string
  Wait for next V430 trigger counter increment

## Slide 7: V430-F Monitor AOI Operation – Failed/No Read
Start_Monitor = TRUE
V430-F Monitor AOI logic
  Confirm V430 in Run Mode
  Wait until V430 trigger counter increments
  Busy = TRUE, Done, Error = FALSE
  Wait for Pass / Fail
    Read Cycle Fail
      Busy = FALSE, Done = TRUE , Error = FALSE
      ErrorID = 1, ErrorMSG = ‘Read Cycle Failed.’
      Barode = ‘’ (cleared, length = 0)
  Wait for next V430 trigger counter increment

## Slide 8: V430-F Monitor AOI Operation – Error States
Good / Bad Read | Done | Barcode | Error | ErrorID | ErrorMSG
Good | TRUE | Decoded string | FALSE | 0 | 
Bad | FALSE |  | TRUE | 1 | Read Cycle Failed.
Bad | FALSE |  | TRUE | 2 | Barcode Data cannot be stored in string data type. Null (0x00) character contained in Barcode Data.
Bad | FALSE |  | TRUE | 3 | Reader not in run mode.

## Slide 9: V430-F Monitor AOI Parameters
Required Parameters
AOI instance name
Assembly_Input
Assembly_Output
Barcode
ErrorMSG
Start_Monitor
Optional Input
Clear_Counters
Monitor_Active
Done
Busy
Error
ErrorID
Trig_Count
Read_Count
Optional Outputs

## Slide 10: V430-F Monitor AOI – Required Parameters
Parameter | Usage | Description
V430_Monitor_Input_MXLSLC_102 |  | AOI instance name
Assembly_Input | InOut | V430-F Input Assembly stored in user-defined data type
Assembly_Output | InOut | V430-F Output Assembly stored in user-defined data type
Barcode | InOut | V430-F barcode string
ErrorMSG | InOut | Message describing error condition (see slide 8)
Start_Monitor | Input | Start monitoring for V430 Read Cycle

## Slide 11: V430-F Monitor AOI – Optional Parameters
Parameter | Usage | Description
Clear_Counters | Input | Clear V430-F EtherNet/IP counters
Monitor_Active | Output | TRUE = AOI logic execution in process
Done | Output | TRUE = V430-F barcode read success
Busy | Output | TRUE = V430-F in read cycle or attempting to enter Run Mode
Error | Output | TRUE = AOI logic error end, barcode data not available
ErrorID | Output | 0 = Barcode read success > 0 = Error & Barcode data not available (see slide 8)
Trig_Count | Output | V430-F EtherNet/IP Trigger Counter
Read_Count | Output | V430-F EtherNet/IP Decode / Matchcode Counter

## Slide 12: Install V430-F EDS file into Studio 5000
Tools (menu) → EDS Hardware Installation Tool
Click Next
Select Register and EDS
Click Next
2
3
4

## Slide 13: Install V430-F EDS file into Studio 5000
Register a single file
Browse your PC for the V430-F EDS file
Click Next
Click Next in the EDS File Installation Test Results window
5
6
7
8

## Slide 14: Install V430-F EDS file into Studio 5000
Click Next in Change Graphic Image window
Click Next in Final Task Summary window
Click Finish to complete the EDS installation
11
9
10

## Slide 15: Add V430-F EtherNet/IP to Studio 5000 project
In the Controller Organizer, Open I/O Configuration, right click on Ethernet and select New Module
12

## Slide 16: Select V430 Module
Type Omron Microscan in the filter box
Select the catalog number that starts with V430 and click Create
Name your V430-F and enter the IP address
Click Change button
14
16

## Slide 17: Select Input MXLSLC Module Definition
Click on the Name drop down selection and select Input MXLSLC
Click the OK button
At the prompt asking “Change module definition?”, click Yes
Confirm the Module settings match what is shown and click OK
18
20

## Slide 18: Confirm V430-F Added to PLC project
Click Close on the Select Module dialog
Confirm V430 is added under Ethernet
22

## Slide 19: Import Add-On Instructions (1 of 2)
In the Controller Organizer, open Assets folder
Right click on Add-On Instruction and select Import Add On-Instruction
Select V430_Copy_Input_MXLSLC_102_AOI.L5X file and click Open
2
4
The Import Configuration dialog provides details on the imported AOI. Click OK when ready to continue

## Slide 20: Import Add-On Instructions (2 of 2)
Right click on Add-On Instruction and select Import Add On-Instruction
Select V430_Monitor_Input_MXLSLC_102_AOI.L5X file and click Open
The Import Configuration dialog provides details on the imported AOI. Click OK when ready to continue
5
7

## Slide 21: Insert V430 Copy AOI into MainRoutine
Expand the folder Tasks, MainTask, MainProgram. Double click on MainRoutine
Drag the V430 Copy AOI into rung 0
8
9

## Slide 22: Set V430 Copy Instance Name
Right click the first element and create a New Tag.
Enter the desired name for this instance and click Create
7

## Slide 23: Set Assembly_Input and Assembly_Output
Right click the Assembly_Input field and create a New Tag.
Enter the desired name and click Create. This tag will be used to retrieve data from the V430-F (e.g., Decoding, Trigger Acknowledge)
Right click the Assembly_Output field and create a New Tag.
Enter the desired name and click Create. This tag will be used to send data to the V430-F (e.g., Trigger)
12
14

## Slide 24: Set Connection_Input and Connection_Output
Double Click on the Connection_Input field. Click the drop down box and expand the V430 (or the name used when adding the V430 module to Ethernet). Select the item V430:I1.Data
Double Click on the Connection_Output field. Click the drop down box and expand the V430 (or the name used when adding the V430 module to Ethernet). Select the item V430:O1.Data
16
17

## Slide 25: Insert V430 Monitor AOI into MainRoutine
Add Rung into MainRoutine
Drag the V430 Monitor AOI into rung 1
19

## Slide 26: Set V430 Monitor Instance Name, Assign Start_Monitor tag
Right click the first element and create a New Tag.
Enter the desired name for this instance and click Create
Right click the Start_Monitor field and create a New Tag.
Enter the desired name for this tag and click Create
Optional – Enter the tag to be used with Clear_Counters
20
22
24

## Slide 27: Set Assembly_Input and Assembly_Output
Double click the Assembly_Input field, click on the dropdown box and select the tag created on step 13, slide 23
Double click the Assembly_Output field, click on the dropdown box and select the tag created on step 15, slide 23
25
26

## Slide 28: Assign Barcode and ErrorMSG tags
Right click the Barcode field and create a New Tag.
Enter the desired name for this instance and click Create
Right click the ErrorMSG field and create a New Tag.
Enter the desired name for this instance and click Create
27
29

## Slide 29: Configure V430-F Read Cycle
Confirm the Read Cycle Sequence settings
Read Cycle = Triggered

## Slide 30: Download to PLC and Run
Download the project to the PLC
Confirm PLC I/O OK
In the Controller Organizer, expand MainProgram and double click Parameters and Local Tags.
Select Monitor Tags to control / monitor PLC tags

## Slide 31: Monitor V430-F from PLC
  Set V430 Monitor AOI Start_Monitor tag = 1, to start monitoring
  V430 read results available, while Done = 1
5