## Slide 1
Technical Note
V430-F Trigger AOI for Rockwell Studio 5000
March 4, 2022

## Slide 2: V430-F Trigger AOI Capabilities
This AOI provides the following functionality:
Trigger V430-F via EtherNet/IP
  Can be used with V430 Read Cycle: Trigger or Start / Stop
  Barcode string output only on good read
  Error on failed read
  AOI to completion time (milliseconds)

## Slide 3: V430-F Trigger AOI Requirements
AOI: V430_Trigger_Input_MXLSLC_102_AOI.L5X
Developed for CompactLogix PLCs using Rockwell Studio 5000 v33
V430-F must be on same subnet as Rockwell CompactLogix PLC
V430-F EIP Assemblies - Input MXLSLC (102) and Output (197) must be used
V430-F read cycle: Triggered or Start / Stop. Presentation (Continuous) mode not supported.
V430 Trigger AOI logic designed to trigger the V430-F; physical triggers should not be used
V430-F End of Read Cycle Mode: Timeout
V430-F Timeout:
  20 to 65535 (milliseconds)
  4 * RPI lower than AOI timeout
Example –
AOI timeout = 2000 (ms), RPI = 10 ms
V430-F Timeout = 2000 – (4 * 10) = 1960 ms

## Slide 4: Copy V430-F EIP Input and Output Assemblies
V430_Copy_Input_MXLSLC_102_AOI.L5X
AOI logic copies every scan
Input: Connection_Input → Assembly_Input
Output: Assembly_Output → Connection_Output
Assembly_Input, Assembly_Output are user defined data types for easier data access.

## Slide 5: V430-F Trigger AOI Operation - Disabled
Execute = FALSE
Busy = FALSE (not in previous read cycle)
Trigger off
  Done, Busy, Error = FALSE
  TotalReadCycleTime, ErrorID = 0
  Barcode, ErrorMSG = ‘’ (cleared, length = 0)

## Slide 6: V430-F Trigger AOI Operation – Good Read
Execute = False (Slide 5)
Set desired Timeout (20 to 65535 milliseconds)
Execute = TRUE
V430-F Trigger AOI logic
  Busy = TRUE,
  Start Timer to check Timeout
  Confirm V430-F online
  Trigger V430-F
  Confirm Trigger Acknowledge
  Wait for Data_Is_Ready
  Read Cycle Pass
    Busy = FALSE, Done = TRUE
    Barode = decoded string
    TotalReadCycleTime = AOI processing time in milliseconds
  Outputs held in this state while Execute = True

## Slide 7: V430-F Trigger AOI Operation – No Read
Execute = False (Slide 5)
Set desired Timeout (20 to 65535 milliseconds)
Execute = TRUE
V430-F Trigger AOI logic
  Busy = TRUE,
  Start Timer to check Timeout
  Confirm V430-F online
  Trigger V430-F
  Confirm Trigger Acknowledge
  Wait for Data_Is_Ready
  Read Cycle Fail
    Busy = FALSE, Error = TRUE
    ErrorID = 1
    ErrorMSG = "Read Cycle Failed.”
    TotalReadCycleTime = AOI processing time in milliseconds
  Outputs held in this state while Execute = True

## Slide 8: V430-F Trigger AOI Operation – Read Cycle Did Not Complete
Execute = False (Slide 5)
Set desired Timeout (20 to 65535 milliseconds)
Execute = TRUE
V430-F Trigger AOI logic
  Busy = TRUE,
  Start Timer to check Timeout
  Confirm V430-F online
  Trigger V430-F
  Confirm Trigger Acknowledge
  Wait for Data_Is_Ready
  Timeout occurs (at step c, d, e, or f)
    Busy = FALSE, Error = TRUE
    ErrorID = (see slide 9)
    ErrorMSG = (see slide 9)
    TotalReadCycleTime = AOI processing time in milliseconds
  Outputs held in this state while Execute = True

## Slide 9: V430-F Trigger AOI Operation – Error States
Good / Bad Read | Done | Barcode | Error | ErrorID | ErrorMSG
Good | TRUE | Decoded string | FALSE | 0 | 
Bad | FALSE |  | TRUE | 1 | Read Cycle Failed.
Bad | FALSE |  | TRUE | 2 | Barcode Data cannot be stored in string data type. Null (0x00) character contained in Barcode Data.
Bad | FALSE |  | TRUE | 3 | Could not enter run mode.
Bad | FALSE |  | TRUE | 4 | Waiting for previous read cycle to complete. Reduce V430 Read Cycle Timeout.
Bad | FALSE |  | TRUE | 5 | Waiting for read cycle to start. Trigger_Acknowledge did not change state.
Bad | FALSE |  | TRUE | 6 | Read Cycle too long.

## Slide 10: V430-F Trigger AOI Parameters
Required Parameters
AOI instance name
Execute
Assembly_Input
Assembly_Output
Barcode
ErrorMSG
Optional Input
Timeout
Optional Outputs
Done
Busy
Error
ErrorID
TotalReadCycleTime

## Slide 11: V430-F Trigger AOI – Required Parameters
Parameter | Usage | Description
V430_Trigger_Input_MXLSLC_102 |  | AOI instance name
Execute | Input | Start Read Cycle
Assembly_Input | InOut | V430-F Input Assembly stored in user-defined data type
Assembly_Output | InOut | V430-F Output Assembly stored in user-defined data type
Barcode | InOut | V430-F barcode string
ErrorMSG | InOut | Message describing error condition (see slide 9)

## Slide 12: V430-F Trigger AOI – Optional Parameters
Parameter | Usage | Description
Timeout | Input | Time limit where AOI logic will terminate and post error if not completed by this time.
Done | Output | TRUE = V430-F barcode read success
Busy | Output | TRUE = AOI logic execution in process
Error | Output | TRUE = AOI logic error end, barcode data not available
ErrorID | Output | 0 = Barcode read success > 0 = Error & Barcode data not available (see slide 9)
TotalReadCycleTime | Output | Time in milliseconds that it took the AOI logic to complete execution.

## Slide 13: Install V430-F EDS file into Studio 5000
Tools (menu) → EDS Hardware Installation Tool
Click Next
Select Register and EDS
Click Next
2
3
4

## Slide 14: Install V430-F EDS file into Studio 5000
Register a single file
Browse your PC for the V430-F EDS file
Click Next
Click Next in the EDS File Installation Test Results window
5
6
7
8

## Slide 15: Install V430-F EDS file into Studio 5000
Click Next in Change Graphic Image window
Click Next in Final Task Summary window
Click Finish to complete the EDS installation
11
9
10

## Slide 16: Add V430-F EtherNet/IP to Studio 5000 project
In the Controller Organizer, Open I/O Configuration, right click on Ethernet and select New Module
12

## Slide 17: Select V430 Module
Type Omron Microscan in the filter box
Select the catalog number that starts with V430 and click Create
Name your V430-F and enter the IP address
Click Change button
14
16

## Slide 18: Select Input MXLSLC Module Definition
Click on the Name drop down selection and select Input MXLSLC
Click the OK button
At the prompt asking “Change module definition?”, click Yes
Confirm the Module settings match what is shown and click OK
18
20

## Slide 19: Confirm V430-F Added to PLC project
Click Close on the Select Module dialog
Confirm V430 is added under Ethernet
22

## Slide 20: Import Add-On Instructions (1 of 2)
In the Controller Organizer, open Assets folder
Right click on Add-On Instruction and select Import Add On-Instruction
Select V430_Copy_Input_MXLSLC_102_AOI.L5X file and click Open
2
4
The Import Configuration dialog provides details on the imported AOI. Click OK when ready to continue

## Slide 21: Import Add-On Instructions (2 of 2)
Right click on Add-On Instruction and select Import Add On-Instruction
Select V430_Trigger_Input_MXLSLC_102_AOI.L5X file and click Open
The Import Configuration dialog provides details on the imported AOI. Click OK when ready to continue
5
7

## Slide 22: Insert V430 Copy AOI into MainRoutine
Expand the folder Tasks, MainTask, MainProgram. Double click on MainRoutine
Drag the V430 Copy AOI into rung 0
8
9

## Slide 23: Set V430 Copy Instance Name
Right click the first element and create a New Tag.
Enter the desired name for this instance and click Create
7

## Slide 24: Set Assembly_Input and Assembly_Output
Right click the Assembly_Input field and create a New Tag.
Enter the desired name and click Create. This tag will be used to retrieve data from the V430-F (e.g., Decoding, Trigger Acknowledge)
Right click the Assembly_Output field and create a New Tag.
Enter the desired name and click Create. This tag will be used to send data to the V430-F (e.g., Trigger)
12
14

## Slide 25: Set Connection_Input and Connection_Output
Double Click on the Connection_Input field. Click the drop down box and expand the V430 (or the name used when adding the V430 module to Ethernet). Select the item V430:I1.Data
Double Click on the Connection_Output field. Click the drop down box and expand the V430 (or the name used when adding the V430 module to Ethernet). Select the item V430:O1.Data
16
17

## Slide 26: Insert V430 Trigger AOI into MainRoutine
Add Rung into MainRoutine
Drag the V430 Trigger AOI into rung 1
9

## Slide 27: Set V430 Trigger Instance Name, Assign Execute tag
Right click the first element and create a New Tag.
Enter the desired name for this instance and click Create
Right click the Execute field and create a New Tag.
Enter the desired name for this tag and click Create
Optional – Change the Timeout to desired value
20
22
24

## Slide 28: Set Assembly_Input and Assembly_Output
Double click the Assembly_Input field, click on the dropdown box and select the tag created on step 13, slide 24
Double click the Assembly_Output field, click on the dropdown box and select the tag created on step 15, slide 24
25
26

## Slide 29: Assign Barcode and ErrorMSG tags
Right click the Barcode field and create a New Tag.
Enter the desired name for this instance and click Create
Right click the ErrorMSG field and create a New Tag.
Enter the desired name for this instance and click Create
27
29

## Slide 30: Configure V430-F Read Cycle
Confirm the Read Cycle Sequence settings
Read Cycle = Triggered
V430 Timeout < AOI Timeout

## Slide 31: Download to PLC and Run
Download the project to the PLC
Confirm PLC I/O OK
In the Controller Organizer, expand MainProgram and double click Parameters and Local Tags.
Select Monitor Tags to control / monitor PLC tags

## Slide 32: Trigger V430-F From PLC
  Set V430 AOI Execute tag (Trigger) = 1, to start a read cycle
  V430 read results available, while Trigger = 1
5