## Slide 1
Mitsubishi PLC iQR/iQF EIP FB Library_V460-H
Vijay Hadagali

## Slide 2: Mitsubishi PLC
The V460 handheld barcode reader can communicate with Mitsubishi PLCs over various communication protocols such as Ethernet IP using a custom function block library designed by Omron engineers for Mitsubishi.

## Slide 3: Mitsubishi iQR/iQF PLC FB Library
Mitsubishi iQR/iQF PLC library defines data types and function blocks for the V460-H handheld reader when communicating via EtherNet/IP to the Mitsubishi iQR/iQF PLCs.
The library’s function blocks allow the Mitusbhi iQR/iQF to trigger, receive results, and adjust settings of the V460-H handheld.
These function blocks are applicable to applications where the V460-H is reading a single barcode or multiple barcodes (up to 10 unique barcodes) and reporting the results to a Mitsubishi iQR/iQF PLCs using Ethernet/IP implicit communication, via the use of tag data links.

## Slide 4
The
Solution
Solution results
User Data Types and FBs for all Assembles
Example programs to trigger and receive results for all Assembles
Test and Debug of example programs
Yes
Yes
Yes
The Mitsubishi function block library is working on Implicit messaging to trigger and receive barcode results.

## Slide 5
System Config
System Configuration Details
V460-H is a multi-code reader that reads 1D &2D barcodes
In a system configuration in which it is connected to a PLC, PC, or other external device, serial commands can be received from, and code reading results can be output to the external device.
The V460-H can be used in the following types of system configurations.
1. Connecting over Ethernet (EtherNet/IP, Serial (TCP), PROFINET)
Using the data link function for each network (excluding Serial), data transfer can be done periodically between the code reader and the external device.

## Slide 6
System
Config
POC product and system configuration details
Basic Control Operations of the Code Reader
The following figure shows basic communications between an external device and the code reader
and the flow of signals and data.
The following methods can be used to exchange data between an external device and the code reader.

## Slide 7
System
Config
System Configuration Details
EtherNet/IP Overview
EtherNet/IP is an industrial multi-vendor network that uses Ethernet. The EtherNet/IP specifications
are open standards managed by the ODVA (OpenDeviceNet Vendor Association). EtherNet/IP is used
by a wide range of industrial devices.
EtherNet/IP Features.
High-speed, High-capacity Data Exchange through Tag Data Links (Cyclic Communications)
The EtherNet/IP protocol supports implicit communications, which allows cyclic communications
(called Tag Data Links) with EtherNet/IP devices.
Tag Data Links are set at the specified communication cycle for each application regardless
of the number of nodes
Data is exchanged over the network at the refresh cycle that is set for each connection
regardless of the number of nodes, the refresh cycle will not increase even if the number of nodes
increase. (Data exchange in the connection is kept in sync)
The refresh cycle can be set for each connection, each application can communicate at its
ideal refresh cycle. (For example, inter process interlocks can be transferred at high speed, while the
production commands and the status monitor information are transferred at low speed.)

## Slide 8
Solution
Details
Solution Details
Ethernet/IP device configurations and Implicit Function Blocks are developed to communicate to the V460 on all Input Assemblies 100, 101, 102, 103, 104, 105 and Output Assemblies 197, 198
Mitsubishi Ethernet/IP device configurations Tool is used to configure device IP address and all Input Assemblies 100, 101, 102, 103, 104, 105 and Out Assemblies 197, 198 details to communicate to Mitsubishi PLC (shown below)
Configuration Tool for Ethernet/IP in Mitsubishi PLC

## Slide 9
102 Function
Block
V460-H EIP 102 Function Block
This function block is applicable to applications where V460-H is reading a barcode and reporting the results to a Mitsubishi iQR/iQF PLC using Ethernet/IP implicit communication, via the use of tag data links.

## Slide 10
102 Function Block
If the function block is enabled without any of the V460_Reader_IN Boolean inputs equal to TRUE, the function block is executing, but no commands are sent to the V460-H.
When one V460_Reader_IN Boolean inputs is set to TRUE, the associated command will be sent to the V460-H. Once the command has been processed, the function will change that input to FALSE (unless controlled by other logic) and another V460_Reader_IN input can be set to TRUE to send the associated command.
Note: With the function block enabled, the function block will report the results, via V460_Reader_OUT, if the V460-H read cycle was initiated by the user pulling the trigger.
The items below must be followed when using the OCR_V460_EIP 102 function block:
The Ethernet/IP Connection must use Input Assembly 102 and Output Assembly 197.
The V460-H Input Assembly 102 DeviceStatus_RunMode must be TRUE for the function block to trigger the unit.
V460-H must not be configured for Presentation (Continuous) mode to use the trigger functionality.
102 Function Block Usage

## Slide 11
105 Function Block
V460-H EIP 105 Function Block
This function block is applicable when the V460-H is reading multiple barcodes (up to 10
unique barcodes) and reporting the results to a Mitsubishi iQR/iQF PLC using Ethernet/IP implicit communication, via the use of tag data links.

## Slide 12
105
Function Block
105 Function Block Usage
The items below must be followed when using the OCR_V460_EIP 105 function block:
The Ethernet/IP Connection must use Input Assembly 105 and Output Assembly 197.
The V460-H Input Assembly 105 DeviceStatus_RunMode must be TRUE for the function block to trigger the unit.
V460-H must not be configured for Presentation (Continuous) mode to use the trigger functionality.
If the function block is enabled without any of the V460_Reader_IN Boolean inputs equal to TRUE, the function block is executing, but no commands are sent to the V460.
When one V460_Reader_IN Boolean inputs is set to TRUE, the associated command will be sent to the V460-H. Once the command has been acted upon by the V460-H, the function will change that input to FALSE (unless controlled by other logic) and another V460_Reader_IN input can be set to TRUE to send the associated command.
Note: With the function block enabled, the function block outputs will update, if the V460-H read cycle was initiated by the user pulling the trigger. For example, after the V460-H trigger is pulled the V460_Busy will change to TRUE during the V460-H read cycle. Once the codes are successfully read the V460_Done changes to TRUE and the decode information is reported in V460_Decode01 to V460_Decode10.

## Slide 13
105 Application
Example
V460-H EIP 105 Application Example
The Application example program Prg_OCR_V460_EIP_105_197_FB designed to report results from multiple barcodes read in V460-H read cycle.
Trigger Reader, receive results and update digital outputs. Program uses input assembly 105 and output assembly 197.

## Slide 14
 | Recommended BOM items for POC solution
1 | Omron V460-H Handheld barcode reader
1 | Mitsubishi - iQR R08 CPU and RJ71EIP91 – EIP Module with associated PLC Rack and Power supply
1 | Mitsubishi – iQF FX5U-32M and FX5-ENETEIP
1 | Mitsubishi – GX Works 3 PLC Engineering/Programming software
1 | Mitsubishi – iQR and iQF EIP Configuration Tool software
Solution
BOM

## Slide 15
Thank You
contact: Vijay Hadagali
Email: vijay.Hadagali@omron.com
web: automation.omron.com
Notes: Closing Corporate slide